## Slide 1: Operating Systems CS3104
Dr Stuart J. Norcross
School of Computer Science

## Slide 2: Key Policy Points
You are assumed to be familiar with the whole student handbook
Read the Good Academic Practice policy
Check that coursework submitted to MMS has been received successfully, and that it’s the right piece of coursework
Coursework submitted after deadline is subject to automatic penalty
Any special circumstances must be documented immediately through the self-certification system, and followed up with coordinator if you are seeking any allowance
You must be available in St Andrews for the entire exam period
info.cs.st-andrews.ac.uk/student-handbook/key-points.html

## Slide 3: Book
Operating System Concepts Essentials, 2nd Ed.
  Silberschatz, Galvin, Gagne
  http://library.st-andrews.ac.uk/record=b2096124

## Slide 4: Additional reading
Operating Systems, 7th Ed
  Stallings
  http://library.st-andrews.ac.uk/record=b1854755
Operating Systems, 3rd Ed.
  Deitel, Deitel, Choffnes
  http://library.st-andrews.ac.uk/record=b1528173
Concurrent Systems
  Bacon
  http://library.st-and.ac.uk/record=b1020055

## Slide 5: Abstract Computer System
Users
System and application programs
  Compilers, Browsers, Text Editors …
Operating System
Computer Hardware

## Slide 6: What is an Operating System?
Software that manages computer hardware
Goals
  Convenience
  Efficiency
  Flexibility

## Slide 7: OS Roles
Resource Allocator
  Manage allocation of hardware resources
  Concerned with fairness and efficiency
Protection Mechanism
  Control execution of applications
  Preventing errors and improper use

## Slide 8: OS Roles
Resource Allocator
  Manage allocation of hardware resources
  Concerned with fairness and efficiency
Protection Mechanism
  Control execution of applications
  Preventing errors and improper use

## Slide 9: Simplest OS
Batch system
  Unit of work is a job
    Program and data
  Automatically switch from one job to the next
  Resident monitor
Notes: Jobs on tape or cards
Memory is split between the OS (monitor) and a single user program.

## Slide 10: Low CPU Utilisation
CPU cannot be kept busy due to IO
job start
job end
CPU busy
CPU idle
Notes: We want the CPU to be busy at all times but if we sequentially execute each jobs from start to finish then the CPU will be idle at some points (because the CPU has to wait on IO).

## Slide 11: Multi-Programming
Subset of jobs held in memory
Improves CPU utilisation
CPU never idle so long as there are jobs to run

## Slide 12: Time-Sharing
Multi-tasking
CPU executes multiple jobs concurrently by switching between jobs quickly
  Users interact with running programs
  Requires low response time
Multiple users share a computer simultaneously

## Slide 13: Course Overview
Important concepts in general purpose time-sharing operating systems
  Processes management
  Main memory management
  Secondary storage management

## Slide 14: Computer Organisation
Overlap of CPU and IO device operation
  Disks, input devices, display (and other output) devices
  Each device is connected to a corresponding device controller
    SATA, USB, graphics device
    Mostly connected to the system’s PCI/PCIe buses

## Slide 15: Interrupt Driven Architecture
Synchronisation between CPU and DCs
Hardware or software can interrupt the CPU
  Cause the CPU to stop what it is doing
  Transfer execution to a routine to handle the interrupt
    Interrupt Service Routine (ISR)

## Slide 16: Types of Interrupt
IO operation completion or error condition
Program interrupts
    divide by zero, illegal instruction, illegal memory access
    Known as traps
Timer interrupts
Hardware failure
OS is interrupt-driven

## Slide 17: Interrupt Handling
Save current program counter
Transfer control to appropriate ISR for interrupt
  May need to save further registers
  ISR executes on per-thread kernel stack
    More on this later
  Potential for interrupt nesting
  Restore register state before return
Transfer control back to original program

## Slide 18: Interrupt Vector
Interrupt vector indexed by device ID
Each element contain the address of the corresponding ISR

## Slide 19: IO with interrupts
CPU writes to registers of DC specifying operation
  CPU continues other processing
DC instructs IO device to perform transfer
  DC interrupts CPU when transfer finished
    Dedicated interrupt stage in CPU cycle
On interrupt:
  program counter saved
  CPU transfers control to the interrupt service routine (ISR) for that device
    address found in interrupt vector
Notes: registers may be part of normal address space
  memory-mapped IO
current job may be suspended waiting for IO
  swap to another job for time being
register contents tell DC what sort of transfer required

## Slide 20: Example Timing
Characters input on 9600 bps serial line
  ISR takes 2 µs to process each interrupt
Notes: 9600/8 = 1200 characters per second
2µs = 2*10-6 s per character
1200*2*10-6 = 0.0024 of every second spent servicing interrupts
~99.8% of the time remains for computation

## Slide 21: Direct Memory Access
Specialised processors for transferring data
  Directly between memory and IO devices
  CPU is not involved
DMA
  Transfers whole blocks at a time
  DMA controller registers
    Source address
    Destination address
    Length
  CPU only interrupted when block transfer completed
Notes: CPU can’t do much work before next word arrives
e.g. for a disk read
  source address on disk
  destination address in memory
CPU can get on with other work while block is being transferred

## Slide 22: CPU, Devices and Memory
DMA I/O Example…

## Slide 23: Reading Recommendation
Overview of process, memory and storage management in a general purpose OS
Operating Systems Concepts Essentials, 2nd Ed.
  Silberschatz, Galvin, Gange
  Sections 1.6, 1.7 and 1.8

## Slide 24: Next Lecture
User processes and privileged operations
System calls

## Slide 25: Questions?